## Slide 1: WF on further details of simulation assumptions for FeCoMP
3GPP TSG RAN WG1 Meeting #86 R1-168253
Gothenburg, Sweden, 22nd – 26th August 2016
Agenda Item: 7.2.14.1
ZTE Corporation, ZTE Microelectronics, Intel, ASTRI, Qualcomm, Ericsson, Nokia, Alcatel-Lucent Shanghai Bell, Samsung

## Slide 2: Proposals
  Add the following details into the simulation assumptions:
    Performance Metric
      Mean, 5%, 50%, 95% user throughput
      Served cell throughput
      Resource utilization (RU)
      Packet arrival rate λ
    Overhead
      3 symbols for DL CCHs, 2 CRS ports and DM-RS overhead according to number of scheduled layers
    Antenna Polarization Model
      Model -2 from 36.873
    Feedback
      PUSCH 3-2 for non-reciprocity operation (PUSCH 3-0 for reciprocity based operation)
      CQI, PMI and RI reporting triggered per 5ms
      Feedback delay is 5 ms

## Slide 3: Proposals
  Baseline schemes are at least below:
    Rel-13 FD-MIMO without coordination for CS/CB
    DPB for NCJT
    Other option can be also used
  Support M=1 in antenna configuration only for small cell layer in evaluation of Scenario D
  Fix the reference errors proposed in R1-167647