## Slide 1: Way forward on Subframes and Slots
Ericsson

## Slide 2: Background
Subframe
  Already agreed upon
  Serves as a numerology-independent clock
Slot
  Typical unit of scheduling for MBB
Mini-slot
  To achieve lower latency than what is possible with a slot transmission
  Potentially useful for unlicensed operation; after LBT transmissions can start earlier than at the slot boundary

## Slide 3: Proposal
Subframe
  Already agreed upon
  Assume x=14 in the reference numerology for subframe definition
Slot
  7 OFDM symbols in the numerology used for transmission (normal CP assumed)
  An integer number of slots fit within one subframe duration
  May contain DL ctrl at the beginning and/or UL ctrl at the end
Mini-slot
  Shorter than 7 OFDM symbols in the numerology used for transmission
  An integer number of mini-slots fit within one subframe duration
  May contain DL ctrl at the beginning and/or UL ctrl at the end

## Slide 4: Example Illustration
subframe
slot
mini-slot
UL and DL dubframes drawn on top of each other, timing advance=0 used for illustration
DL and UL
DL only
UL only
data or ctrl
data
data or ctrl
Example of slot usage
Example of subframe and slot structure