## Slide 1: WF on observations on UE impact aspects of NB-IoT positioning
Huawei, HiSilicon, …
R1-168333
3GPP TSG RAN WG1 Meeting #86
Gothenburg, Sweden, August 22-26, 2016
Agenda item 7.2.11.1.4

## Slide 2: Background
The Rel-14 NB-IoT enhancements WID asks RAN1 to study both UTDOA and OTDOA for NB-IoT, and to provide recommendation to RAN#73 as the basis to make a choice
A way forward for reporting to RAN#73 was agreed in RAN1#86 and the observations on the following aspects regarding UE impacts should be reported:
  Report changes UE complexity compared to Rel-13 NB-IoT
  Report total impact to UE battery life

## Slide 3: Observations
Impact to UE implementation/complexity
  For OTDOA, UE needs to support
    LTE Positioning Protocol (LPP) to communicate with E-SMLC via eNB.
    Measurements for positioning to get downlink RSTD of the set of configured neighboring cells.
  For UTDOA, UE needs to support
    Configuration and transmission of UL positioning signal.
Impact to UE power consumption
  For OTDOA, the UE power consumption for positioning includes the power consumed by any DL signaling, signal processing (e.g., measurements) and UL reporting of the measurements of the set of configured neighboring cells for the purpose of positioning
  For UTDOA, the UE power consumption for positioning includes the power consumed by any DL signaling, and transmitting UL signal for the purpose of positioning
  NOTE (to be removed): Numerical results on battery life impact have not been included as they provided by only one company