## Slide 1
3GPP TSG-RAN1 Meeting #86 R1-16nnnn
Gothenburg, Sweden, 22- 26 August 2016
Agenda Item 7.2.4.2.2
Way Forward on Inclusive Hybrid CSI-RS Framework
Ericsson, ZTE Corporation, ZTE Microelectronics, Nubia, Xinwei, ITRI, ASTRI, …

## Slide 2: BACKGROUND
There is RAN1 interest in many, diverse, potential use cases and implementations of hybrid CSI-RS reporting from RAN1#85
  Many different CSI reporting combinations are proposed to support these use cases
    6 high level mechanisms
    12 mechanism-option combinations
  Use cases target different eNB implementations, UE complexity simplifications, and/or CSI-RS overheads
Mechanisms 2A, 2B, and 3
  Optimize CSI reporting for particular, limited, combinations
  Exclude other CSI reporting combinations
Mechanisms 4 and 5
  Enable this diversity of use cases and implementation
  Require very little specification effort

## Slide 3: Proposal
Hybrid CSI reporting with CSI process or resource pairs is supported
  TM10 UEs support process pairs; TM9 UEs support resource pairs
    For TM9, different CSI-RS resources and/or CSI reporting configurations can be used for PUCCH and PUSCH
  Techniques or constraints need to be specified to reduce UE complexity at least for TM9
    Alt-1: UE calculates one CSI report for only one process of a pair, or resource of a pair, at a time
      TM10 can be configured with multiple process pairs
    Alt-2: Define the period of the 1st eMIMO-Type as N times of the period of the 2nd eMIMO-Type, where N>1
  Rel-13 CSI process configurations are supported
    A report for either eMIMO-type can contain any Rel-13 CSI, including e.g. CQI, PMI, and RI
The number of mechanisms/options that restrict what CQI/RI/PMI/CRI is reported per eMIMO-type is minimized, preferably to:
  Hybrid CSI reporting with one CSI process, where:
    Class A reporting in the first eMIMO-type
    Class B K=1 in the second eMIMO-type