## Slide 1: WF on simulation assumption for NB-IoT positioning
ZTE, Ericsson, Nokia, Alcatel-Lucent Shanghai Bell, Huawei, Hisilicon
R1-168363
3GPP TSG RAN WG1 Meeting #86
Gothenburg, Sweden, August 22-27, 2016
Agenda item 7.2.11.1

## Slide 2
Parameters | Description
Cellular Layout | Hexagonal grid, 19 cell sites, 3 sectors
Frequency band | 900 MHz
Inter site distance | 1732 m
Sampling rate | Reported together with simulation results
Antenna configuration | BS: 2Tx2Rx; NB-IoT UE: 1Tx1Rx
Rx noise figure | BS: 3 dB, NB-IoT UE: 5dB
Thermal noise density | -174 dBm/Hz
BS Tx power | 43 dBm for Standalone. For inband and guardband, total 46 dBm for 10 MHz LTE. NB-IoT DL anchor carrier is assumed to have 6 dB power boosting No power boosting on non-anchor DL carrier.
NB-IoT UE Tx Power | 23 dBm and 20 dBm, optionally consider low power class(es) UE
Path loss model | L=I + 37.6log10(R), R in kilometers; I=120.9
Shadowing standard deviation | 8 dB
Correlation distance of Shadowing | 110 m

## Slide 3
Parameters | Description
Shadowing correlation | Between cell sites: 0.5 Between sectors of the same cell site: 1.0
Antenna pattern (horizontal) | See table 5-7, 3GPP TR 45.914, 65°H-plane.
BS antenna gain | 18 dBi
NB-IoT UE Antenna gain | -4 dBi
BS cable loss | 3 dB
Frequency reuse | 1
Network synchronization error | See Table 5.1.1-1 in TR 37.857
Interference modeling | Three Load levels ( 0.1/0.5/1.0 ) Note: Load is the prob. of effective interferer in each neighboring cell using the same time frequency resources for positioning reference signal
Positioning reference signal design | Report together with simulation results
Radio resources used by positioning | Report together with simulation results (with consideration of transmission gap)
Residual frequency error | Randomly chosen from the set {-50,50} Hz
Frequency drift | 22.5Hz/s
UL transmission timing error modelling | According to RAN4 requirements

## Slide 4: User Distribution
Indoor scenario
  All UEs are indoor
  UE distribution follows TR 45.820
  Channel model :ETU, 1Hz and EPA,1Hz
  Building Penetration Loss Scenario#1 Coef =0.5 (See Annex D.1 of TR 45.820).
Outdoor scenario
  All UEs are Outdoor
  UEs are uniformly dropped
  Channel model : ETU, 2.5Hz 25Hz and EPA,2.5Hz 25Hz
  Optional Channel model : ETU, 100Hz and EPA,100Hz
  No Building Penetration Loss