## Slide 1: WF on URLLC System Capacity Definition Clarification
Intel, Qualcomm Inc.
3GPP TSG RAN WG1 Meeting #86 R1-168398
Gothenburg, Sweden, 22nd - 26th August 2016
Agenda item - 8.1.7

## Slide 2: Background
At RAN1#85, the URLLC system capacity metric was agreed:
  “The following performance metrics are defined for evaluation and feature selection in RAN1 (FFS the method of evaluation, including whether SLS are required):
    URLLC capacity is defined as delivered traffic given the (L, R) constraint
      Denoted as C(L,R)
    URLLC / eMBB multiplexing capacity is defined as the simultaneously delivered URLLC capacity C(L,R) and eMBB capacity T”
Clarification is needed how capacity is calculated

## Slide 3: Proposal
System level evaluation method is used for URLLC system capacity study to analyze impact from inter-cell interference, queueing and scheduling latency, multiplexing with other services
URLLC system capacity is calculated as follows:
  C(L, R) is the maximum offered cell load under which Y% of UEs in a cell operate with target link reliability R under L latency bound
  X = (100 – Y) % is the percentage of UEs in outage
  A UE in outage is defined as the UE can not meet latency L and link reliability R bound
    X include at least UEs which reliability target is not met due to queueing and interference
    X may include UEs which have channel attenuation less then the MCL needed to achieve the link reliability
  Companies report their assumption on X