## Slide 1: WF on definition of UL grant-free resource
Huawei, HiSilicon, CATR, CATT,
China Telecom, CMCC, Convida Wireless, Fujitsu, Intel, Spreadtrum, InterDigital, Oppo, Orange,
[Samsung], [ZTE], [Nokia], […]
3GPP TSG RAN WG1 #86 R1-16xxxx
Gothenburg, Sweden, Aug. 22-26, 2016
Agenda item: 8.1.2.2

## Slide 2: Background
Agreement:
At least the following options for “autonomous/grant-free/contention based” UL transmission should be studied
  Opt. 1: a UE performs random resource selection
    Details FFS
  Opt. 2: a UE’s resource is pre-configured by eNB or pre-determined
    Details FFS
Other options are not precluded

## Slide 3: Proposals
A resource for “autonomous/grant-free/contention based” UL transmission is defined by a time-frequency block and a MA signature
A MA signature includes at least one of the following
  Codebook
  Code/Sequence
  Interleaver and/or mapping pattern
  Demodulation reference signal
  Preamble