## Slide 1: WF on URLLC evaluation parameter and LLS method
Huawei, HiSilicon, CATR, […]
3GPP TSG RAN WG1 Meeting #86 R1-168371
Gothenburg, Sweden, 22 – 26 Aug 2016
Agenda Item: 8.1.7

## Slide 2: Background
In RAN1#85, URLLC evaluation metric was discussed.
In RAN#72, it was agreed that URLLC study will target complete in Rel-15.
Evaluation metrics, methods, and evaluation parameters need to be further discussed to facilitate URLLC evaluation.
  Evaluation metrics to consider RAN1 and RAN inputs.
  Evaluation method for each of the evaluation metric.
  Evaluation configuration to consider traffic model and detailed evaluation parameters.
Reliability as fundamental KPI for URLLC study, LLS is considered. Motivation of LLS include:
  Investigate PHY layer design impact on reliability, including frame structure, numerology, together with other design components
  To obtain under what channel condition can NR achieve desired level of reliability within specific latency bound

## Slide 3: Proposal
Evaluation metric and evaluation method for URLLC
  User plane latency :
    Definition: Follow the definition in TR38.913, target value is 0.5ms one way, without reliability requirement.
    Evaluation method: Analytical; re-transmission is considered, but scheduling / queuing delay is not included in analytical evaluation
  Reliability
    Definition: Reliability is defined as the success probability R of transmitting X bits within L seconds, which is the time it takes to deliver a small data packet from the radio protocol layer 2/3 SDU ingress point to the radio protocol layer 2/3 SDU egress point of the radio interface, at a certain channel quality Q (e.g., coverage-edge).
      Denoted as R(L, Q, SE), where SE is the required spectral efficiency and SE=X/L/B where B (in Hz) is the user bandwidth that is allocable to one device.
      The latency bound L includes transmission latency, processing latency, retransmission latency and queuing/scheduling latency (including scheduling request and grant reception if any)
    Evaluation method: Link level simulation as start point
  URLLC capacity and URLLC / eMBB multiplexing capacity
    Definition: Follow RAN1#85 agreements with further clarification, if needed
    Evaluation method: System-level simulation can be considered

## Slide 4: Proposal
Traffic model for URLLC evaluation
Packet arrive rate Companies report the used option, and are encouraged to provide how to exploit arrival rate for Option 2 | Option 1: periodically Option 2: Poisson arrival with arrival rate l
PHY Packet size | 32 byte, 50 byte, 200 byte Other values are not precluded.

## Slide 5: Proposal
LLS parameter for URLLC evaluation
Attributes | Values or assumptions
Carrier Frequency | 700MHz and 4 GHz (FDD and TDD)
Modulation and coding rate | QPSK, 16QAM, 64QAM 1/12, 1/6, 1/3 Other MCS not precluded Comparison should be made for the same spectrum efficiency
User bandwidth | Companies report
PHY Packet size | 32 byte, 50 byte, 200 byte Other values are not precluded.
Latency bound (NOTE1) | 1ms Other values are not precluded Companies report delay assumption, e.g., processing delay, transmission delay, re-transmission delay. Scheduling / queuing delay is not assumed in LLS.
SINR range | -5dB to 20dB Larger range is not precluded
Sub-carrier spacing | Companies report
TTI length | Companies report
OFDM symbols per TTI | Companies report
Channel model | TDL/CDL in TR38.900; user speed = 3km/h, 15km/h (other user speed is not precluded)
BS antenna configuration | 2/4/8 Tx/Rx ports as start point Other values (i.e., up to 256) are not precluded
UE antenna elements | 2/4 Tx/Rx ports as start point Other values (i.e., up to 8) are not precluded
ACK Feedback assumption | Ideal as start point NOTE: It is also possible that no ACK feedback is needed,
Channel estimation | Ideal as start point; Realistic is not precluded when RS design is ready
CQI feedback assumption | Companies report the feedback scheme if any
NOTE1: Proponents are encouraged to report under what SINR the proposed scheme could achieve 99.999% reliability within the latency bound
NOTE2: control channels including DL assignment/UL grant/ACK/NACK are to be evaluated further.

## Slide 6: Proposal
RAN1 first focuses on reliability evaluation using link level simulation.
The following link level simulation method is applied to evaluate reliability
  For one drop, sufficient number of packets will be generated according to the traffic model. And user bandwidth B Hz, and an average SNR Q will be set.
  For one data packet, if it is successfully received within latency boundary L’ (with or without re-transmission), this packet is regarded as successfully received. Otherwise, this packet is regarded as failed.
  Latency L’ captures transmission latency, processing latency, and retransmission latency, but without scheduling / queuing latency.
    If average scheduling latency is assumed to be Lsche, then L’=L0- Lsche, where L0 is the total latency boundary including scheduling / queuing latency.
  Reliability R (L’,Q, SE)= N/M, where N is the successfully received number of packets within the latency boundary L’, and M is the total number of packets generated in the simulation.