## Slide 1: Use Cases/Scenarios for Slot Structure Discussion
Qualcomm Incorporated
3GPP TSG RAN WG1 #86 R1-168489
Gothenburg, Sweden, 22nd- 26th August 2016
Agenda item: 8.1.6

## Slide 2: Transmission duration (symbols NCP)
Nokia/Huawei: EMBB 7 for all, may have <7 for special cases
Qualcomm: EMBB 15/30kHz 14, 120kHz 28/14
  Defined as duration between scheduling decisions in EMBB and uplink control
Panasonic: EMBB 15kHz 2,5,6,7,14, >15kHz 0.5ms or 0.125ms
ZTE: EMBB 15kHz 2 (FDD only),7,14
DCM: EMBB most SCS 7, 14, and higher SCS x7, x14 (15kHz LTE short TTI)
Mediatek: EMBB 15/60kHz 7, 240kHz 28 and <7 for URLLC
Motorola: EMBB 15kHz 2,7,14, >15kHz 7
CATT: EMBB 7 for all (from UE perspective)

## Slide 3: Transmission duration (symbols NCP)
Ericsson: EMBB 7/14/28 (not all multiples), URLLC 2
  Control may not be in front of ever transmission duration
LGE: EMBB 14 for all, 2 and multiple of 2
Intel: EMBB 14 for all licensed, may have <14 for special cases
  Defined as duration between scheduling decisions in EMBB and uplink control if any
Samsung: EMBB 14 for all licensed, may have <14 for URLLC
Interdigital: EMBB 14, 28 for all, URLLC 2 for 15kHz, 4 for 30kHz, 7 for 60kHz
Fujitsu: EMBB 15kHz 1,2,5,6,7,14, 30kHz >2, 60kHz >4 (not including guard)
  Interval between DL control e.g., 3,7, and 14 (configurable)

## Slide 4: Observations and Notes
Observations
  Many consider EMBB (NCP) 15kHz 14
    Some support through aggregation from 7
  Many considering multiples of basic value e.g., 2 or 7
    Gap generation may be difficult depending on assumptions
    Gap overhead
    Where to send control channel?
Notes
  Companies may have different notions of what can be included in the transmit duration
  All multiples included unless otherwise specified
  Guard may be taken from symbols listed above in some cases