## Slide 1
3GPP TSG-RAN1 Meeting #86 R1-168511
Gothenburg, Sweden, 22- 26 August 2016
Agenda Item 7.2.4.2.1
Way Forward on Antenna Port Layouts
Ericsson, QUALCOMM, Intel, CATT, ATT, DOCOMO,Verizon

## Slide 2: Background (1/2)
Conclusions from RAN1#85:
  Class A codebook enhancement:
    Starting from Rel-13 Class A codebook design structure by enabling different N1 and N2 combinations
  Reduce the number of combinations of codebook parameters (N1, N2, O1, and/or O2)
    To be concluded in RAN1#86
    Examples:
      Down select from 19 (N1,N2) combinations; and/or
      Reduce the number of (O1,O2) combinations
  Other possibilities are not excluded

## Slide 3: BACKGROUND (2/2)
1D antenna port layouts can provide significantly better performance than 2D antenna port layouts with the same number of antenna ports (R1-167639)
1D 1x16 antenna array is much smaller than most macro antennas deployed
      1x16 antenna is about 1.2m long at 2GHz, which is 1.7x shorter than typical 2m long antennas today. It’d be even smaller at >2GHz
    Codebook complexity is not a reason for 2D over 1D
  For a 32 ports 4x4 array with (8,8) oversampling, there are (8*4)*(8*4)=1024 2D beams
  For a 32 port 16x1 array with 8x oversampling, there are 8*16=128 beams, which requires less processing than the 2D array
1D antenna deployment is practical (R1-167639)
  Low-rise buildings are the norm in light urban & suburban areas of North America: UE population is distributed uniformly in azimuth
  Mounting 1D antennas sideways on wall of buildings (e.g. building parapet) is practical and visually unobtrusive
  Wind load and weights are not worse than 2D antennas of the same size on towers
Chart: Performance of 1D vs. 2D Port Layout ( 3D UMa)
| 8x2 | 4x4 | 2x8 | 1x16
Mean user throughput | 0 | 0.1 | 0.21 | 0.32
Cell-edge user throughput | 0 | 0.21 | 0.44 | 0.68
# of antenna elements | Element spacing (λ) | Antenna size (cm) |  | 
 |  | 2GHz | 3.5GHz | 4GHz
16 | 0.5 | 120 | 69 | 60
1D 1x16 Antenna sizes:
Typical existing 17dBi antenna size at 800-900MHz: 2.6m

## Slide 4: Proposal
Simplify 1D configuration
  Drop the (1,N2) rows (with red text)
    Single design can be used for (N1,1) and (1,N2).
Reduce UE computational complexity
  Remove (8,8) combinations for 20, 24, 28, 32 ports (with green text)
    Reduces number of beams by 2
    Limited performance gain from (8,8) vs. (8,4)
Number of CSI-RS antenna ports, P | (N1,N2) | (O1, O2)
20 ports | (2,5) | (8,4), (8,8)
 | (5,2) | (8,4), (4,4)
 | (10,1) | (4,-),(8,-)
 | (1,10) | (-,4),(-,8)
24 ports | (3,4) | (8,4), (8,8)
 | (4,3) | (8,4), (4,4)
 | (2,6) | (8,4), (8,8)
 | (6,2) | (8,4), (4,4)
 | (12,1) | (4,-),(8,-)
 | (1,12) | (-,4),(-,8)
28 ports | (2,7) | (8,4), (8,8)
 | (7,2) | (8,4), (4,4)
 | (14,1) | (4,-),(8,-)
 | (1,14) | (-,4),(-,8)
32 ports | (8,2) | (8,4), (8,8)
 | (2,8) | (8,4), (4,4)
 | (4,4) | (8,4),(4,4)
 | (16,1) | (4,-),(8,-)
 | (1,16) | (-,4),(-,8)
N & O Combinations Based on Rel-13
with Potential Simplifications