## Slide 1: WF on PUCCH retuning for BL/CE UE
Ericsson, Samsung, NEC, Qualcomm, Virtuosys, Sony, Sierra Wireless, NTT DoCoMo, AT&T, Intel
R1-168514
AI 7.1.5
3GPP TSG RAN WG1 Meeting #86
Gothenburg, Sweden, 22nd 26th August 2016

## Slide 2: Background
Issues with the currently specified way to create guard periods for BL/CE UEs during PUCCH retuning through rate matching were discussed in the following contributions:
  R1-166498 On timeline issues with shortened PUCCH format Qualcomm
  R1-166630 Simulation results for PUCCH frequency retuning NEC
  R1-166684 PUCCH Structure for Frequency Retuning Samsung
  R1-167848 PUCCH frequency retuning for BL/CE UE Ericsson
  R1-168461 WF on PUCCH retuning for BL/CE UE Ericsson
  R1-168465 Operation Alternatives for PUCCH Retuning Samsung

## Slide 3: Background (from 36.211)

## Slide 4: Proposal
All BL/CE UEs have mandatory support for:
  PUCCH retuning gap creation through puncturing
  Legacy (i.e. normal and type-0 shortened) PUCCH formats
UE capability signalling indicates whether a BL/CE UE also supports:
  PUCCH retuning gap creation through shortened PUCCH formats
  Additional shortened PUCCH formats type-1 and type-2
The eNB can RRC configure a capable BL/CE UE to use either
  PUCCH retuning gap creation through puncturing, or
  PUCCH retuning gap creation through shortened PUCCH formats.
The eNB can optionally indicate in [SIB1-BR] that BL/CE UEs should only use orthogonal sequence index #0 for PUCCH format 1/1a/1b transmission.
Ask RAN2 to introduce signalling for above points 2, 3 and 4.