## Slide 1
WF on further clarification on grant-free transmission for mMTC
LG Electronics, Huawei, HiSilicon, ETRI, [Mediatek],
R1-168538
3GPP TSG RAN WG1 #86
Gothenburg, Sweden, 22nd – 26th August 2016
Agenda item 8.1.2.2

## Slide 2: Background
Agreements drawn by R1-168257
  At least the following options for “autonomous/grant-free/contention based” UL transmission should be studied
  Opt. 1: a UE performs random resource selection
    Details FFS
  Opt. 2: a UE’s resource is pre-configured by eNB or pre-determined
    Details FFS
  Other options are not precluded
Agreements on terminologies
A MA physical resource for “grant-free” UL transmission is comprised of a time-frequency block
  Note: spatial dimension is not considered as a physical resource in this context
A MA resource is comprised of a MA physical resource and a MA signature, where a MA signature includes at least one of the following:
  Codebook/Codeword
  Sequence
  Interleaver and/or mapping pattern
  Demodulation reference signal
  Preamble
  Spatial-dimension
  Power-dimension
  Others are not precluded
Details on MA physical resource and MA signature resource FFS

## Slide 3: Proposal
A MA signature pool is composed of multiple MA signatures, including
  e.g., Sequence/Interleaver/Interleaver mapping pattern/Demodulation reference signal/Preamble/Spatial-dimension/Power-dimension
  Combination of above examples and others are not precluded
For grant-free transmission,
  MA physical resource(s) is pre-configured/pre-defined and re-configurable
  Opt.1:
    MA signature pool can be pre-defined/pre-configured
    Alt 1: a UE randomly selects a MA Signature from MA Signature Pool
    Alt 2: A UE choose MA signature with a pre-configured/pre-defined rule
  Opt.2 :
    MA signature(s) can be pre-configured or pre-determined

## Slide 4: Appendix
Possible arrangements on the categorization
  Opt.1:
    MA signature pool can be pre-defined/pre-configured
    a UE randomly selects a MA Signature in MA Signature Pool
  Opt.2 :
    Opt. 2-1. MA signature pool can be pre-configured
      A UE choose MA signature with a pre-configured/pre-defined rule
    Opt. 2-2. MA signature(s) can be pre-configured or pre-configured