## Slide 1: Way forward on observations for eMBB data channel coding
Samsung, Qualcomm Incorporated, Nokia, ASB, KT Corporation, Intel Corporation,
3GPP TSG RAN WG1 Meeting #86bis R1- 1610690
Lisbon, Portugal 10th - 15th October 2016
Agenda item: 8.1.3.1

## Slide 2: Background
Conclusion of RAN1#86:
The eMBB data channel coding scheme will be chosen at RAN1#86bis
  including agreeing on the observations that led to the decision.
Companies are encouraged to:
  continue analysis and comparison in order to inform the final decision at RAN1#86bis
  provide any remaining details, especially focusing on LDPC (in view of the situation in this meeting)
  provide any remaining details of the flexibility requirements and how they can be satisfied, and corresponding implementation complexity and any impact on performance
Note that consideration of combinations of coding schemes is not precluded.
In case of changes to proposals already available, companies are encouraged to provide them at least 1 week before the normal submission deadline for RAN1#86bis.

## Slide 3: Observation: Summary
Observation
  LDPC codes can efficiently support the whole range of eMBB data channel rates, block lengths, and IR HARQ with fine granularity
  LDPC codes can provide better area and energy efficiency than other coding schemes, especially for high throughput
  LDPC codes are amenable to parallelization and can provide better decoding latency

## Slide 4: Observation: Rate flexibility
  LDPC code can support multiple codes rates, and HARQ, including IR-HARQ by extension of parity check matrix
    Multiple LDPC code families can be compactly and efficiently described
    Decoder does not need to carry complexity of mother code on early transmissions, and performance is comparable to Turbo codes
    Survey of some results on implementation complexity in RAN1#86 and RAN1#86bis:
Company | Tdoc number | Observations
Ericsson | R1-1608875 | LDPC can support rate flexibility
LG | R1-1609239 | LDPC can support rate flexibility
ZTE | R1-166414/R1-1608974 | LDPC can support rate flexibility
MediaTek | R1-167532 | LDPC can support rate flexibility
Intel | R1-166558/R1-1610377 | LDPC can support rate flexibility
Nokia, ASB, Verizon, Xilinx | R1-167274 | LDPC can support rate flexibility
Qualcomm | R1-1610137 | LDPC can support rate flexibility
Samsung | R1-166770/R1-1609064 | LDPC can support rate flexibility
National Taiwan University | R1-1609708 | LDPC can support rate flexibility

## Slide 5: Observation : Length flexibility
  Shortening together with lifting and rate-matching allows LDPC code support information block size and codeword length flexibility with 1-bit granularity
    The additional HW complexity for supporting a flexible LDPC code with arbitrary sub-block size is not a problem, as compared with that of inflexible LDPC codes.
    Survey of some results on implementation complexity in RAN1#86 and RAN1#86bis:
Company | Tdoc number | Observations
Ericsson | R1-1608875/R1-1608876 | LDPC can support length flexibility
LG | R1-1609242 | LDPC can support length flexibility
ZTE | R1-166414/R1-1608974 | LDPC can support length flexibility
MediaTek | R1-167532 | LDPC can support length flexibility
Intel | R1-166557/R1-1610377 | LDPC can support length flexibility
Nokia, ASB, Verizon, Xilinx | R1-167273 | LDPC can support length flexibility
Qualcomm | R1-1610137 | LDPC can support length flexibility
Samsung | R1-166769/R1-1609065 | LDPC can support length flexibility
National Taiwan University | R1-1609708 | LDPC can support length flexibility

## Slide 6: Observation : Implementation
  LDPC implementation complexity can be better than other codes when LDPC can support flexibility
    The energy and area efficiencies of a flexible LDPC decoder is better than those of LTE turbo codes.
    Survey of some Tdocs on implementation complexity in RAN1#86 and RAN1#86bis:
Company | Tdoc number | Observations
Qualcomm | R1-1610139 | LDPC better than Turbo/Polar
ZTE | R1-1608971 | LDPC* better than Turbo/Polar
Ericsson | R1-1608879 | Depends on how different parity check matrices
Intel | R1-1609511 | LDPC better than Turbo/Polar
Mediatek | R1-1609337 | A flexible barrel shifter supporting lifting factors up to 384 occupies only 7% of the decoder.
Nokia, ASB, Verizon, Xilinx | R1-1609582 | LDPC better than Turbo/Polar
Samsung | R1-1609067 | LDPC better than Turbo
LG | R1- 1609241 | Flexible shift network (QSN) requires twice more multiplexer than single size shift network (SS-CS)
* (Small size of based matrix, lift size of NR LDPC has the form of N*2K)

## Slide 7: Observations : Performance
LDPC codes can support stable performance for various MCS with fine granularity, comparable or better to other codes with similar decoding complexity
  Performance comparison among best cases for candidates from data sharing shown below:
References: Enhanced turbo (R1-166929), LTE Turbo (R1-167889), QC-LDPC (R1-1610140), PC-Polar (1608864) provided from RAN1 #86 and RAN1 #86bis submissions.
Required SNR for 4-QAM and BLER = 1.0%

## Slide 8: Observation (from 167999)
  Implementation complexity point of view, LDPC is better than other coding schemes especially for high throughput
    Survey of some results on implementation complexity in RAN1#86:
Company | Tdoc number | Observations
Qualcomm | 166372 | LDPC better than Turbo/Polar
ZTE | 167896 | LDPC better than Turbo/Polar
Ericsson | 166396 | Inflexible LDPC better than Turbo Flexible LDPC comparable to Turbo Polar list decoder little worse than Turbo
Intel | 166557 | LDPC better than Turbo/Polar
Mediatek | 167531 | LDPC better than Turbo
Nokia, ASB, Verizon, Xilinx | 167272 | LDPC better than Turbo/Polar
Samsung | 166774 | LDPC better than Turbo
Interdigital | 167567 | LDPC better than Turbo/Polar
LG | 167884 | Some LDPC* comparable with Turbo
* Limited flexible LDPC