## Slide 1: WF on resource reselection
Samsung, CATT, Huawei, HiSilicon, LGE, ZTE, …
3GPP TSG RAN WG1 Meeting #87 R1-1613124
Reno, Nevada, USA November 14 – 18, 2016
Agenda item - 6.1.8

## Slide 2: Background
In RAN1#86, it was agreed that
  UE is not required to perform PSSCH-RSRP measurement in a TTI that occurs before the reception of a successfully decoded associated SA.
    UE applies the PSSCH-RSRP measured in a TTI that occurs at or after the reception of a successfully decoded associated SA to a TTI that is indicated by the SA but occurs before the reception of the SA.

## Slide 3: 2 transmissions for a TB
If UE only receives one SA, resource exclusion should be done based on both two transmissions
If initial transmission is before subframe n while retransmission is after subframe n, a UE can derive PSSCH-RSRP of the retransmission and do resource exclusion accordingly

## Slide 4: Proposals
UE applies the PSSCH-RSRP measured in a resource indicated by a successfully decoded associated SA to the other resource indicated by the SA but located outside the sensing window
If UE only receives the first SA scheduling a TB with two transmissions, UE does resource exclusion corresponding to the reserved resources of both transmissions
If initial transmission is before subframe n while retransmission is after subframe n, UE does resource exclusion in step 2 based on the scheduled retransmission resource