## Slide 1: WF on NR CSI Acquisition
AT&T, Samsung, NTT Docomo, Intel, Qualcomm, ZTE
3GPP TSG RAN WG1 Meeting #87
Reno, USA 14th –18th November 2016
Agenda: 7.1.3.3
R1-1613143

## Slide 2: Motivation
NR should support multiple levels of CSI granularity in spatial, frequency and time domain as following examples:
  In spatial domain, different rank and/or CSI type (I or II) are of different beam resolution.
  In frequency domain, wideband or subband CSI report is of different granularity
Many factors need to be considered when deciding the CSI granularity in each domain, the following are some examples:
  UE wireless Channel, e.g. large DS means -> subband CSI report.
  Feedback channel capacity and overhead.
  Traffic QoS
  Scheduling plan: e.g. SU-MIMO or MU-MIMO
Observations: UE should be involved to decide the CSI granularity according to the channel it observed.

## Slide 3: Proposal
Study the benefit of involving UE in selecting CSI report setting based on its channel measurement.
  CSI report setting may include the granularity of spatial domain (CSI type I or II, rank) and frequency domain (e.g. wideband/subband or subband size).
  UE selection is under certain constraint configured by network.
Study UE assisted/selected CSI report setting, with the following use cases:
  Example-1: UE may recommend the best CSI report setting to help network configure CSI feedback. (Network can overwrite UE’s recommendation)
  Example-2: Network can configure multiple candidate CSI report settings for UE to select, and UE indicates its selection along with CSI report (e.g. “Enhanced” RI can be used for UE to indicate its selection)
Note: LTE actually support multiple types of UE selected feedback “format”:
RI (may change the payload of the CSI)
CRI (may change the payload of the CSI)
Orthogonal beam pattern for Rel. 13 Rank 3-4 codebook (no impact on the payload of the CSI)