## Slide 1: WF on Preamble Format Design
NTT DOCOMO, ETRI, ZTE
3GPP TSG RAN WG1 Meeting #87
Reno, USA 14th – 18th November 2016
Agenda: 7.1.2.3
R1-1613169

## Slide 2: Proposals
  For the consecutive multiple/repeated RACH preambles,
    Option 1: CP is inserted at the beginning of the consecutive multiple/repeated RACH sequences, CP/GT between RACH sequences is omitted and GT is reserved at the end of the consecutive multiple/repeated RACH sequences
    Option 2: The same RACH sequences with CP is repeated and GT is reserved at the end of the consecutive multiple/repeated RACH sequences
    Option 3: The same RACH sequences with CP/GT is repeated
    For options 2 and 3, the same RACH sequences with and without CP/GT can be further multiplied with different orthogonal cover codes and transmitted.
    For example, the consecutive multiple/repeated RACH preambles would be used when Tx/Rx beam correspondence does not hold at either TRP or UE
  For a single RACH preamble, CP/GT are required for each RACH preamble
    For example, the single RACH preamble would be used when Tx/Rx beam correspondence held at both TRP or UE for multi-beam operation

## Slide 3: Proposals
The BW for a RACH preamble transmission is targeted to not be wider than 5 MHz for a carrier frequency of below 6 GHz and not wider than X MHz for a carrier frequency ranging from 6GHz to 52.6 GHz
  X could be, e.g., 5, 10, and 20MHz
At least, one reference numerology for RACH preamble is defined, e.g.,
  1.25 x 2^n kHz
  15 x 2^n kHz
    Integer value of n is FFS
  Other values are not precluded
Based on the reference numerology for RACH preamble, multiple RACH preambles with scalable numerologies are supported depending on the carrier frequency

## Slide 4: Proposals
The following sequences can be considered for the evaluation
  ZC sequence
  m-sequence
Companies are encouraged to provided their proposed sequence length