## Slide 1: WF on UL MIMO Waveform for NR
Samsung, Ericsson, Nokia, Alcatel-Lucent Shanghai Bell, AT&T, CATT
3GPP TSG RAN WG1 Meeting #86bis
Reno, USA 14th - 18th November 2016
Agenda item: 7.1.3.1
R1-1613174

## Slide 2: Background
The following was agreed in RAN1#86bis:
  NR Support DFT-S-OFDM based waveform complementary to CP-OFDM waveform, at least for eMBB uplink for up to 40GHz
    FFS additional low PAPR techniques
    CP-OFDM waveform can be used for a single-stream and multi-stream (i.e. MIMO) transmissions, while DFT-S-OFDM based waveform is limited to a single stream transmissions (targeting for link budget limited cases)
    Network can decide and communicate to the UE which one of CP-OFDM and DFT-S-OFDM based waveforms to use
      Note: both CP-OFDM and DFT-S-OFDM based waveforms are mandatory for UEs

## Slide 3: Proposal
When a UE is configured with UL SU-MIMO transmission with rank adaptation from rank-1 to rank-LMAX, CP-OFDM waveform is used for L-layer transmission where L=1, 2, …, LMAX
  LMAX is the maximum number of layers