## Slide 1: WF on CSI Framework for NR
Samsung, AT&T, NTT DOCOMO, [Ericsson]
3GPP TSG RAN WG1 Meeting #86bis
Reno, USA 14th - 18th November 2016
Agenda item: 7.1.3.3
R1-1613175

## Slide 2: Background
The following was agreed in RAN1#86bis:
  CSI-related settings consisting of:
    CSI reporting settings
      CSI parameter can be independently configured, e.g. time and/or frequency granularity, FFS: ON/OFF
        FFS: Details of configurability
      Definition of CSI parameters (e.g., CQI, PMI, RI) is FFS
    RS (at least for CSI measurement) settings, e.g. CSI-RS (CSI-IM as a special case)
      FFS: Other RS for CSI measurement
    CSI measurement settings
      To configure which RS setting is used for a particular CSI reporting setting
  Study the case where a UE can be configured with:
    N CSI reporting settings
    M RS (for CSI measurement) settings
    CSI measurement setting configures mapping/linkage between N CSI reporting and M RS settings

## Slide 3: Proposal
A UE can be configured for CSI acquisition via higher-layer signalling with the following features:
  N≥1 CSI reporting settings, M≥1 RS settings, and a CSI measurement setting which links the N CSI reporting settings with the M RS settings
  A CSI reporting setting includes at least the following:
    Time-domain behavior: aperiodic or periodic/semi-persistent
    Frequency-granularity, at least for PMI and CQI
    Which CSI parameters are reported
      If PMI is reported, PMI Type (Type I or II) and codebook configuration
  An RS setting includes at least the following:
    Time-domain behavior: aperiodic or periodic/semi-persistent
    RS type which encompasses at least CSI-RS
    RS resource set of K resources
  A CSI measurement setting includes at least the following :
    One CSI reporting setting
    One RS setting

## Slide 4: Proposal
Study the possibility of configuring a UE with multiple CSI measurement settings including dynamic indication to select a preferred CSI measurement setting
  Including selection of resource(s) out of the K resources within an RS setting

## Slide 5: Example configuration
An example use case:
  One RS setting is intended for horizontal domain channel measurement
  One RS setting is intended for vertical domain channel measurement
  One RS setting is intended for measuring the channel between uncorrelated antenna elements (such as cross-polarization and sub-panels)
  4 CSI reporting settings are configured.
    3 CSI reporting setting (each is corresponding to one RS setting) to obtain CSI report
    1 CSI reporting setting is linked to multiple RS settings for CQI report
      CQI report hypothesis is based on the channel measurement from multiple RS settings.
      Detail CQI hypothesis is FFS, a starting point is assuming Kronecker product of the channel observed in each RS setting.

## Slide 6: Example configuration: illustrated
CSI reporting setting-1
2Tx DFT Codebook
CSI reporting setting-2
4Tx DFT Codebook
CSI reporting setting-3
4Tx DFT Codebook
CSI reporting setting-4
CQI report with the hypothesis: V×H×U, where the V, H and U are observed channel from RS setting 1/2/3 separately
(× is Kronecker Product)
RS setting-1 2Tx CSI-RS (Vertical domain)
RS setting-2 4Tx CSI-RS (Horizontal domain)
RS setting-3 2Tx CSI-RS (Cross-polarization)