## Slide 1: WF on DCI Design in TDD
CATT, LGE, CMCC, Huawei, HiSilicon, Samsung, Xinwei
3GPP TSG RAN WG1 Meeting #87 R1-1613200
Reno, USA 14th - 18th December 2016
Agenda item – 6.2.1.1.1

## Slide 2: Background
RAN1#86 agreement:
Time location of the initial transmission is the first subframe included in the resource pool on the V2V carrier that occurs after 4 ms from the DCI transmission subframe.
SL cross-carrier scheduling timing needs to be considered in order to enable scheduling all the V2V subframes.

## Slide 3: Background
There are reserved bits considering current discussed payload size difference between DCI 0 and DCI 5A in TDD
Some V2V subframes in dedicated V2V carrier cannot be scheduled yet when V2V subframes are scheduled by any DL subframe in TDD Uu carrier

## Slide 4: Background
D
S
U
U
U
D
S
U
U
U
Figure 1. legacy behavior based on TDD UL/DL configuration 0
V
V
V
V
V
V
V
V
V
V
V
V
V
0
1
2
3
4
5
6
7
8
9
Uu carrier
PC5 carrier
0
1
2
3
4
5
6
7
8
9
D
S
U
D
D
D
D
D
D
D
Figure 2. legacy behavior based on TDD UL/DL configuration 5
V
V
V
V
V
V
V
V
V
V
V
V
V
0
1
2
3
4
5
6
7
8
9
0
1
2
3
4
5
6
7
8
9
Uu carrier
PC5 carrier

## Slide 5: Proposals
If the DCI for SL SPS or dynamic scheduling is transmitted in subframe n and the offset value (in two-bit field) is set to m, the time location of initial transmission is the first subframe included in the resource pool that occurs at or after subframe n+4+m.
  Offset value is one of {0, 1, 2, 3}.
  Applicable to both SL SPS and dynamic scheduling.
  Subframe n including all available DL subframes, special subframes in TDD Uu carrier.