## Slide 1: Cross-link interference mitigation for flexible duplex
Huawei, HiSilicon, Intel
3GPP TSG RAN WG1 #87 R1-1613221
Reno, USA
14th – 18th November 2016
Agenda item: 7.1.6.2
Document for decision

## Slide 2: Background
Conclusion:
  Continue study considering some or all of the following aspects:
    Deployment scenarios/bands, same-/cross-operator considerations
    Resource assignments and rate adaptations
    Frame structure and HARQ/scheduling timing
    Measurements for cross-link interference management
    Signalling (e.g., OTA, backhaul, UE capability, etc.)
    Cross-link interference management (IC/IS, power control, etc.)
    Centralized vs. distributed interference/resource management
    Beamforming/MIMO
    Duplex modes (e.g., FDD/TDD, FDM/TDM, etc.)
    Latency reduction
    Whether or not LTE interference/resource management can be used as a starting point (as applicable)
    Sensing
    RS design
    Advanced receiver
    Timing alignment between DL and UL
Agreements:
  Strive for a common framework for cross-link interference mitigation schemes for both paired and unpaired spectra

## Slide 3
At least following cross-link interference mitigation schemes should be supported for NR flexible duplex with and without the assumption on inter-cell coordination:
  Advanced receiver for interference cancellation/suppression
  Sensing based scheme
  Power control
  Coordinated beamforming/scheduling
  Link adaptation
RAN1 should support symmetric RS and timing alignment between DL and UL to enable above schemes.
Cross-link interference mitigation schemes can be commonly applicable for both paired and unpaired spectrum.
Proposal