## Slide 1: WF on resource allocation for larger PDSCH/PUSCH channel bandwidth
ZTE, ZTE Microelectronics, Sequans, [Qualcomm], …
3GPP TSG RAN WG1 Meeting #86bis R1-1613293
Reno, USA 14th - 18th November 2016
Agenda Item: 6.2.8.1.4

## Slide 2: Proposal -1
Distributed resource allocation is supported for PDSCH with 5 MHz larger channel bandwidth in CE mode A, which is down-selected from the following alternatives:
  Alt 1: Staring narrowband Index(or wideband index) + NB bitmap + Resource allocation within existing narrowband
  Alt 2: Starting narrowband Index (or wideband index) + bitmap of RBG within 5-MHz wideband
  Alt 3: Wideband index + distributed allocation based on Resource allocation type 2 within wideband (including localized/distributed flag)

## Slide 3: Proposal - 2
Continuous resource allocation is supported for PUSCH with 5 MHz larger channel bandwidth in CE mode A, which is down-selected from the following alternatives :
  Alt 1: Staring narrowband Index(or wideband index) + existing PUSCH type 0 within 5-MHz wideband
  Alt 2: Existing PUSCH type 0 (RIV limited)
  Alt 3: Staring RB index + number of RBs

## Slide 4: Appendix for Proposal - 1
 | Starting narrowband/Wideband index (bits) | RA bits | localized/distributed flag | Total overhead (bits) | Scheduling flexibility
Alt-1 | 2 or 4 | 8 | - | 10 or 12 | The starting position is limited within a narrowband/wideband RA unit is RB
Alt -2 | 2 or 4 | 8 | - | 10 or 12 | The starting position is limited within a narrowband/wideband RA unit is RBG=3PRBs
Alt-3 | 2 | 7 or 9 | 1 | 10 or12 | starting position is limited within a wideband 1 or 2 PRB-level granularity both localized/distributed.
Comparison (20 MHz system bandwidth)

## Slide 5: Appendix for Proposal - 2
 | Starting narrowband index /Wideband index (bits) | RA ( bits) | Total overhead (bits) | Scheduling flexibility
Alt-1 | 4 | 9 | 13 | starting position of RA is limited within a narrowband
Alt-2 | 0 | 12(if RIV value is limited to 2500) | 12 | starting position of RA is unlimited
Alt-3 | 7 | 5 | 12 | starting position of RA is unlimited
Overhead comparison (20 MHz system bandwidth)