## Slide 1: WF on sPUCCH sTTI mapping
Ericsson, LG Electronics, Huawei, HiSilicon, Nokia, Alcatel-Lucent Shanghai Bell, Samsung, NTT DOCOMO, CATT, ZTE, ZTE Microelectronics, Intel
R1-1613326
3GPP TSG RAN1 #87
Reno, Nevada (US), Nov 14 - 18, 2016
Agenda item 6.2.10.2.3

## Slide 2: Background
The sTTI mapping of the sPUCCH is still not decided upon
For sPUSCH a flexible design of data symbols and DMRS is considered for the 2os sTTI while for 4os (if adopted) and 7os sTTI, the mapping is determined.
Such flexible design is not appropriate for sPUCCH where multiplexing between sPUCCH UEs and potentially multiplexing between sPUCCH UEs and PUCCH UEs should be possible.

## Slide 3: Proposal
For a given UE, a sPUCCH format follows a fixed sTTI mapping where the same sTTI boundaries, data symbol placements (except the last symbol in the subframe - depending on SRS) and DMRS symbol placements (if used) are the same in every subframe.