## Slide 1: Way forward on reduced interruption of SC-MTCH reception due to SC-MCCH acquirement
Huawei, HiSilicon
R1-1613346
3GPP TSG RAN WG1 Meeting #87
Reno, Nevada, November 14-18, 2016
Agenda item 6.2.9.2

## Slide 2: Background(1/2)
For NB-IoT SC-PTM, RAN2 has agreed:
  SC-MCCH for feMTC and NB-IoT is scheduled dynamically.
  RAN2 assumes that direct Indication or similar mechanism (that provides information in DCI) can be used for SC-MCCH change notification. RNTI is FFS.
For an UE who has not been receiving any ongoing SC-MTCH, UE needs to detect new session start based on the SC-MCCH change notification;
For an UE who has been already receiving one ongoing SC-MTCH, UE would need to acquire SCPTMConfiguration message by at least detecting the search space of SC-MCCH at the beginning of every MP, if no indication on change of configuration of the ongoing SC-MTCH is informed to the UE;

## Slide 3: Background(2/2)
NB-IoT UE cannot monitor search space of SC-MTCH or receive NPDSCH of SC-MTCH while UE is monitoring search space for SC-MCCH;
For UE receiving the SC-MTCH, the mechanism that UE acquires SCPTMConfiguration message at the beginning of every MP will cause interruption of SC-MTCH reception at the beginning of a MP, even when the configuration of the interested SC-MTCH has not been changed at all in the MP.

## Slide 4: Proposals 1
The DCI format scheduling an NPDSCH of a SC-MTCH includes a field to indicate whether the configuration of the associated SC-MTCH will be changed or removed in the next MP:
  FFS: the indicator field also includes one bit to indicate new session start in the next MP if the UE is interested in detection of new session arrivals;
For UEs that have been receiving ongoing SC-MTCH are not required to monitor the search space of SC-MCCH in the next MP unless:
  There is a DCI detected in the current MP for scheduling an NPDSCH of the on-going SC-MTCH indicates that the configuration of the associated on-going SC-MTCH will be changed in the next MP;
  or there is no DCI detected for scheduling SC-MTCH in the current MP;
  FFS: The indicator in the DCI detected in the current MP for scheduling the on-going SC-MTCH indicates a new session start in the current MP;

## Slide 5: Proposals 2
The DCI format for SC-MCCH scheduling is used to indicate SC-MCCH change notification;