## Slide 1: WF on sTTI scheduling
Huawei, HiSilicon, Ericsson, CATT, NTT DOCOMO , Intel, Nokia, [Qualcomm] …
3GPP TSG RAN1 #87
Reno, USA Nov 14 - 18, 2016
Agenda Item: 6.2.10.2.2
R1-1613373

## Slide 2: Background
Agreement
Select a sTTI scheduling scheme among the following candidates for each sTTI length
  Single level DCI
    RRC configuration of sPDCCH search space and/or sPDCCH frequency region
    UE-specific information in sDCI related to sPDSCH/sPUSCH
  Two level DCI
    RRC configuration may or may not at least partially indicate sPDCCH frequency region/search space for some of the variants described below
    variant 1
      Slow DCI: non UE-specific information in PDCCH
      Fast DCI: UE-specific information in sDCI
    variant 2
      Slow DCI: UE-specific information in PDCCH
      Fast DCI: UE-specific information in sDCI
    variant 3
      Slow DCI: UE-specific information in PDCCH and/or sPDCCH
      Fast DCI: UE-specific information in sDCI
  Note: the sTTI scheduling scheme may be the same or different for different sTTI length
FFS how to reduce the payload of sDCI/DCI messages for sTTI operation
FFS support of multi-sTTI scheduling
Additional L1 signaling related to sTTI operation can be considered

## Slide 3: Proposal
A sPDSCH/sPUSCH is scheduled by a UE-specific sDCI (sDCI 1)
sDCI in PDCCH region (sDCI 2) dynamically indicates the adjustment of sPDCCH search space and/or frequency resource for the following sTTI(s), from a RRC configured sPDCCH search space and/or frequency resource set
  If the UE does not detect the sDCI2, the UE may monitor the RRC configured sPDCCH search space and/or frequency resource set
  [include “Activation/deactivation information of sDCI 1 monitoring” in sDCI 2]
      Other information in sDCI2 is not precluded
      FFS whether sDCI2 is UE-specific or common or group
FFS: The sDCI in PDCCH region may not be transmitted in every subframe