## Slide 1: WF on CBR measurement of PUE
Samsung, ZTE, …
3GPP TSG RAN WG1 Meeting #87 R1-1613466
Reno, Nevada, USA November 14 – 18, 2016
Agenda item - 6.2.1.4.1

## Slide 2: Proposal
In RAN1#86bis, it was agreed that
  Channel busy ratio (CBR) is defined for the congestion measurement over PC5 in V-UEs
    CBR is the portion of sub-channels whose S-RSSI exceed a (pre-)configured threshold observed during (working assumption: 100 ms).
      Only the sub-channels included in the resource pool are used for the measurement.
      FFS whether additional separated measurement is needed for SA pool.
    For a UE in Mode 3, the eNB indicates a set of resources on which the UE perform this measurement
    For a UE in Mode 4, the measurement is pool-specific.
      A UE measures at least on its current TX pool(s).
        FFS whether a UE measures on a pool which is not its current transmission pool.
      RAN1 will not optimize this measurement to address the case of multiple TX pools
  UE Reporting of CBR to eNB is supported
    Details up to RAN2 including any possible additional averaging at higher layer

## Slide 3: Proposals
At least in a configured transmission pool adopting partial sensing, a PUE measures CBR in the resource subset that the PUE sensed to support resource reselection