## Slide 1: WF on sensing operation
LG Electronics, CATT
3GPP TSG RAN WG1 Meeting #87
Reno, US 14th - 18th November 2016
Agenda item: 6.1.8
R1-1613472

## Slide 2: Background
RAN1 received two LSs from RAN2 on sensing operation:
  R1-1613316 on use of exceptional pool
  R1-1613317 on resource reservation issue

## Slide 3: Proposals
Proposal on R1-1613316
  Send a response LS informing that RAN1 has no concern on RAN2 agreements and working assumption in the LS.
Proposal on R1-1613317
  RAN1 agrees that the issues can be solved under the current RAN1 specifications if resource reselection is triggered if any of the following three conditions is met:
    There is no more resources in the configured sidelink grant and there is new MAC PDU to be transmitted.
    UE does not transmit on reserved resources for one second.
    UE skips N consecutive transmission opportunities where N is (pre)configured in the range [1, 9] and it is (pre)configured to use this condition.