## Slide 1
Way Forward on Two-Step RACH Fallback
Nokia, Interdigital
3GPP TSG RAN WG1 #87 R1-1613547
Reno, Nevada, USA, 14th – 18th November 2016
Agenda item: 7.1.2.5

## Slide 2: Background
Agreements:
RAN1 is studying and some companies see potential benefits of a simplified RACH procedure consisting of two main steps (Msg1 and Msg2) for UEs
RAN1 has discussed the following:
  The use of a UE identity in Msg 1
  Msg 2: RA response that is addressed to the UE identity in Msg 1
  FFS on the definition and choice of the UE identity
  FFS on the applicability scenarios of simplified RACH procedure
RAN1 to send LS to RAN2
RAN1 is aware that RAN2 is also studying the RACH procedure and RAN1 would like to inform RAN2 to take the above into considerations and would like to request any feedback on UE identities and associated procedure and also ask the corresponding applicable scenarios

## Slide 3: Way Forward
2-step RACH procedure falls back to 4-step RACH procedure when Msg.1 preamble is detected while Msg.1 data signal is not detected.
  If Msg. 1 data signal is not detectable, the Msg. 1 preambles are acknowledged by sending Msg. 2 with the content of the 4-step Msg. 2
  Msgs. 3 and 4 transmissions follow like in 4-step procedure