## Slide 1: WF on UTDOA positioning in NB-IoT
Ericsson, Nokia, ASB, Qualcomm, Verizon, Sony, Samsung …
R1-1613564
3GPP TSG RAN WG1 Meeting #87
Reno, USA, November 14-18, 2016
Agenda Item: 6.2.9.1.3

## Slide 2: Background
Current progress of the UTDOA based positioning discussion
  Proposed observations on use of Rel-13 NPRACH for UTDOA:
  It is possible to configure NPRACH resources such that the eNB can provide a dedicated resource for UTDOA positioning
    In these configurations, in scenarios where there is mixed use of NPRACH for positioning and normal purposes there would be impact to
      System capacity
      NPRACH intra-cell and inter-cell interference
      Battery life and latency of UEs in other NPRACH resources
  RAN1 concludes its verification of UTDOA in Rel-13.
  Inform RAN3, RAN4 of the above.

## Slide 3: Background
There is currently no common understanding of the feasibility of using Rel-13 NPRACH based UTDOA positioning for NB-IoT.
  In some contributions, e.g., R1-1612603 and R1-1611140, it is pointed out in few scenarios it might be possible to use Rel-13 NPRACH based UTDOA positioning for NB-IoT.
  In other contributions, e.g., R1-1611119, R1-1611305, R1-1611631, and R1-1611120, it is pointed out that by taking all the practical constraints, it is not feasible in practical NB-IoT networks to use Rel-13 NPRACH based UTDOA positioning for NB-IoT as well as the positioning accuracy is questionable.

## Slide 4: Proposed Conclusion
RAN1 understands the limitations and difficulties of using Rel-13 NPRACH signal for UTDOA based positioning.
The use of Rel-13 NPRACH signal for UTDOA based positioning is not practically feasible due to significant instability caused by interference when using Rel-13 NPRACH signal for UTDOA based positioning as well as excess UL resource consumption.
It is proposed RAN1 does not further evaluate UTDOA based position for NB-IoT for Rel-14.
  This does not preclude the study of UTDOA based positioning for NB-IoT in future releases.