## Slide 1
3GPP TSG-RAN WG1 #87 R1-1613582
Reno, USA, 14th – 18th November, 2016
WF on codebook structure for NR
Intel, Samsung, CATT, Huawei
Agenda item: 7.1.3.3

## Slide 2: Proposal
Precoding vectors in the NR codebook has W=W1W2 structure
  FFS on additional support of W3 (location of W3 matrix is FFS), e.g. multi-panel support, analog beam selection
  W1 is WB and W2 can be WB or SB.
  Vector of W1 can be configured to the UE
    Examples of W1 vectors: orthogonal W1, non-orthogonal W1
    W1 vectors corresponding to one panel to another panel can be different
For W, NR supports DFT-based and non-DFT based precoding vectors
  FFS construction of non-DFT based precoding for W
    e.g. beam broadening function applied to DFT-based vectors in W1
      high rank SU-MIMO, high mobility UEs
    e.g. linear combining vectors