## Slide 1: Way forward on CRS awareness on CRS+PRS for OTDOA
Intel Corporation, Acorn Technologies
R1-1613586
3GPP TSG RAN WG1 Meeting #87
Reno, USA, November 14- 18, 2016
Document for: Decision
Agenda Item: 6.2.6.1

## Slide 2: Background
Agreement in RAN1#87
  Support the use of CRS together with PRS for OTDOA enhancement
    If CRS usage together with PRS is configured,
      Signal CP information for CRS if PRS is present.
        Note: this CP information signaling is additional one to the existing CP signaling for PRS.
      Quasi-collocation between PRS and CRS is assumed.
      FFS signaling of CRS presence (e.g., due to MBSFN subframes)

## Slide 3: Background
When CRS+PRS for OTDOA is configured, the CP types for both CRS and PRS are signaled to UE.
Cases according to CP types
  Case1: {normal CP for CRS, normal CP for PRS}
    UE can know PRS is transmitted MBSFN subframe, non-MBSFN subframe, or both, but UE does not know the exact MBSFN subframe configuration.
    Thus, UE can use CRS in subframe #0, #4, #5, #9, and can use the first OFDM symbol in other subframes.
  Case2: {normal CP for CRS, extended CP for PRS}
    UE can know PRS is transmitted on MBSFN subframe only.
    Thus, UE can fully utilize all available CRS.
  Case3: {extended CP for CRS, normal CP for PRS}
    This is not valid configuration.
  Case4: {extended CP for CRS, extended CP for PRS}
    UE can know PRS is transmitted MBSFN subframe, non-MBSFN subframe, or both, but UE does not know the exact MBSFN subframe configuration.
    Thus, UE can use CRS in subframe #0, #4, #5, #9, and can use the first OFDM symbol in other subframes.

## Slide 4: Proposal
Signal one bit in LPP per each reference cell and neighbour cell indicating whether or not the MBSFN subframe configuration of reference/neighbour cell is the same as the primary serving cell of the UE