## Slide 1: WF on rate matching for 5MHz BL UEs
Intel Corporation
R1-1613587
3GPP TSG RAN WG1 Meeting #87
Reno, Nevada, USA, 14th – 18th Nov 2016
Agenda item 6.2.8.1.2

## Slide 2: Background
Agreement from RAN1 #87 meeting:
Soft buffer size for 5-MHz BL UE is 73152 bits (75% of full buffer size corresponding to a max TBS of 4008 bits and 8 DL HARQ processes).
Rate matching and the number of DL HARQ processes for purpose of soft buffer size determination:
    Option 1: Limited Buffer Rate Matching (LBRM) with 25% reduction of buffer size
      8 DL HARQ processes assumed for purpose of soft buffer size determination
    Option 2: Full Buffer Rate Matching (FBRM)
      6 DL HARQ processes assumed for purpose of soft buffer size determination
FFS: Down-select between Options 1 and 2.
The same soft buffer size (73152 bits) applies to 5-MHz BL UE supporting 10 DL HARQ processes.

## Slide 3: Proposals
PDSCH rate matching for 5-MHz BL UEs uses Limited Buffer Rate Matching (LBRM) with 25% reduction of buffer size, corresponding to mother code rate of 4/9