## Slide 1: WF on Reduced Control Overhead for Multicast
Nokia, Alcatel-Lucent Shanghai Bell, Qualcomm, [], []
R1-1613615
3GPP TSG RAN WG1 Meeting #87
Reno, USA, 14th-18th November 2016
Agenda item 6.2.4.1.1

## Slide 2: Background
In RAN2#95-Bis, the following working assumptions were agreed :
  Agreements on RRC configuration
  SC-MCCH for feMTC and NB-IoT is scheduled dynamically.
  We assume we need to support large values for SC-MCCH modification period, repetition period. Exact values FFS
For Release 13, SPS is only supported for BL/CE UEs in CEModeA.
No strong use case was identified for the support of CEModeB SPS in Release 13.

## Slide 3: BACKGROUND
For SC-MTCH different TBs would ideally be sent using the same physical layer parameters such as MCS, repetition level, number of PRBs if there are no scheduling constraints
Control and Data may be TDMed and hence subframes used for control may not be usable for PDSCH
  Always true for NB-IOT
  Depends on the allocation for eMTC
Sending a different PDCCH for each PDSCH will hence be inefficient from a network resource and UE power consumption point of view
Methods that reduce control such as single MPDCCH/NPDCCH for multiple PDSCH or use of SPS would hence be useful

## Slide 4: Proposal
RAN1 should consider the following methods to reduce control overhead for SC-MTCH
One PDCCH can schedule multiple PDSCH
  A 2-bit numPDSCHindicator mapping to values [{1,2,4,8}] is included in the DCI to support this.
  Other parameters are the same for all the PDSCH scheduled using the same DCI
  The PDSCH can be scheduled back-to-back with predetermined gap
SPS can be used to support the scheduling of a SC-MTCH
  To support SPS for a specific SC-MTCH, the SC-MCCH SCPTMConfiguration message provides for that SC-MTCH the:
    • SPS-C-RNTI
    • numberOfConfSPS-Processes
    • semiPersistSchedIntervalDL
  For SPS semiPersistSchedIntervalDL parameter is extended to support values greater than sf640.
  FeMTC UEs in RRC_Idle mode and at all PRACH CE levels, can have SPS activated and released for SC-MTCH, by DCI

## Slide 5: Proposal
Gmax for SS containing
SPS ACT/REL DCI
SPSconfigDL:
semiPersistSchedIntervalDL
SPS PDSCH
(each block represents 1 set of R repetitions)
SPS DCI
Search Space
Unlike conventional SPS, where the PDCCH that the UE monitors for SPS DCI occurs with every subframe, it is possible to configure the Gmax of the SPS DCI search space to ensure that monitoring of the SPS DCI is not required for each PDSCH transmission.