## Slide 1: WF on Signaling Design for MUST Case 3
MediaTek, CMCC, III, ITRI, Huawei, HiSilicon
R1-1613616
3GPP TSG-RAN WG1 #87
Reno, USA, 14th – 18th November 2016
Agenda item 6.2.3.2

## Slide 2: Proposals
For DCI format 2B or Rel-13-DMRS-table not configured or Rel-13-DMRS-table=0
  UE expects k_max = 1 in this case
  2 bits are added to carry assistance information for predefined antenna port of interfering layer provided in Table 1
    00: No assistance information
    01: MUST interference is present with QPSK
    10: MUST interference is present with 16QAM
    11: MUST interference is present with 64QAM

## Slide 3: Proposals
For DCI formats 2C and 2D and Rel-13-DMRS-table=1
  When k_max=1, total 4 bits are added to carry assistance information
    2 bits (denoted as B) with the message provided in Table 2
    2 bits for MOD of the single interfering layer
      00: QPSK
      01: 16QAM
      10: 64QAM
      11: 256QAM
  When k_max=3, total 7 bits are added to carry assistance information for predefined ordered antenna ports of interfering layers provided in Table 3
    The assistance information for each port is represented with 5 states
      State 1: no assistance information
      State 2: interference present with QPSK
      State 3: interference present with 16QAM
      State 4: interference present with 64QAM
      State 5: interference present with 256QAM
    Total 125 states are required when number of layers of desired signal=1 and OCC length=4
    Total 25 states are required when number of layers of desired signal=2 and OCC length=4
    Total 5 states are required when number of layers of desired signal=1 and OCC length=2
    7 bits are required for assistance information

## Slide 4
Table 1 | 
Antenna port of target UE | Port with assistance information
7 | 8
8 | 7
Table 2 |  |  |  | 
Antenna port of target UE | Port with assistance information |  |  | 
 | B=00 | B=01 | B=10 | B=11
7 | No assistance information | 8 | 11 | 13
8 |  | 7 | 11 | 13
11 |  | 7 | 8 | 13
13 |  | 7 | 8 | 11
Note: when B=00, UE ignores the assistance information of MOD |  |  |  | 
Table 3 |  |  |  |  | 
Number of layers of desired signal=1 and OCC length=2 |  | Number of layers of desired signal=1 and OCC length=4 |  | Number of layers of desired signal=2 and OCC length=4 | 
Antenna port of target UE | Ordered ports with assistance information | Antenna port of target UE | Ordered ports with assistance information | Antenna ports of target UE | Ordered ports with assistance information
7 | 8 | 7 | 8, 11, 13 | 7, 8 | 11, 13
8 | 7 | 8 | 7, 11, 13 | 11, 13 | 7, 8
 |  | 11 | 7, 8, 13 |  | 
 |  | 13 | 7, 8, 11 |  |