## Slide 1
WF - Outcome from offline discussion about mini slots
ZTE, ZTE Microelectronics, Intel, Interdigital, Ericsson, Motorola, Nokia, ASB, Samsung, Panasonic, LGE, Huawei, Hi Silicon, CATT, Docomo , [Qualcomm]
R1-1613630
3GPP TSG RAN WG1 #87
Reno, USA, 14th – 18th November 2016
Agenda item 7.1.1

## Slide 2: Proposal
Mini-slots have the following lengths
    At least above 6 GHz, mini-slot with length 1 symbol supported
      FFS below 6 GHz including unlicensed band
      FFS for URLLC use case regardless frequency band
    FFS whether DL control can be supported within one mini-slot of length 1
    Lengths from 2 to slot length -1
      FFS on restrictions of mini-slot length based on restrictions on starting position
      For URLLC, 2 is supported, FFS other values
    Note: Some UEs targeting certain use cases may not support all mini-slot lengths and all starting positions
    Can start at any OFDM symbol, at least above 6 GHz
      FFS below 6 GHz including unlicensed band
      FFS for URLLC use case regardless frequency band
    A mini-slot contains DMRS at position(s) relative to the start of the mini-slot