## Slide 1: WF on DL control channel for URLLC
Huawei, HiSilicon,CATR,Potevio
3GPP TSG RAN WG1 Meeting #87 R1-161335
Reno, Nevada, USA, November 14 - 18, 2016
Agenda item: 7.1.4.4

## Slide 2: Background
Reliability requirement for URLLC
  A general reliability requirement for URLLC is 99.999% for X bytes within a user plane latency of 1ms according to 36.913.
The robustness of both control channel and data channel have impact on the overall reliability
  Based on R1-1611221,even assuming two shot transmissions is allowed within delay bound, the reliability requirement (99.999%) can never be met if the associated control channel conveying DL assignment is operated at 1% miss detection probability. Also, in order to improve the resource utilization, it is preferred that the control channel reliability should be relatively higher so that the BLER target for the data transmission can be relaxed.

## Slide 3: Proposal
  NR should support the error probability of DL control channel for URLLC less than 1% compared to LTE requirement (1%),
    FFS value,e.g.,0.001%,0.01%,0.1%
    Study the following options to ensure the DL control channel reliability
    Minimize the DCI payload size
      E.g., limited TB sizes and BW allocation
      E.g., only consist of the control information that related to data reception/decoding directly in the control channel region
    Adopt high aggregation level ,e.g.,16 and 32
    Exploit the multi-path diversity, e.g. spatial/frequency/carrier
    Interference coordination for URLLC control channel
    Power boosting for URLLC control channel