## Slide 1: WF on beam management for control and data channel
3GPP TSG RAN WG1 Meeting #87 R1-1613670
Reno, USA, 14th – 18th November 2016
Agenda Item: 7.1.3.3
ZTE, ZTE Microelectronics, ASTRI, Intel, Samsung, LGE

## Slide 2: Background
  The following agreements on control and data channel have been reached:
    Support using same or different beams on control channel and the corresponding data channel transmissions
  Regarding beam related indication, it has been agreed that
    For downlink, NR supports beam management with and without beam-related indication
      When beam-related indication is provided, information pertaining to UE-side beamforming/receiving procedure used for data reception can be indicated through QCL to UE
        FFS: Information other than QCL
  Separate beam selection can be considered for DL control and data channel transmission, due to the following aspects:
    Transmission schemes and their associated beams may be different for each of them due to own purposes for throughput and robustness, etc.
    In a multi-TRP scenario, control channel and data channel can be transmitted from different TRPs.

## Slide 3: Proposal
  For downlink control channel, NR supports beam management with and without beam-related indication
    When beam-related indication is provided, information for assisting UE-side beamforming for the blind decoding/reception of downlink control channel implies QCL assumption between antenna ports for control channel demodulation RS and antenna ports for beam management RS w.r.t. spatial parameter for the demodulation of downlink control channel.
    FFS: details for indication signaling (e.g. DCI, MAC CE, RRC)
  FFS: DL control and data channels share the same beam resource pool at least for beam-related indication
    e.g. A beam resource pool is a pool of reference signal resources for beam-related indication.
  Study separate beam-related indication for DL control and data channels within the shared beam resource pool