## Slide 1: WF on UL URLLC transmission without grant
ZTE, ZTE Microelectronics, InterDigital, Nokia, …
3GPP TSG RAN WG1 Meeting #87 R1-1613726
Reno, USA, 14th – 18th November 2016
Agenda item: 7.1.4.4
Document for decision

## Slide 2: Background
Agreements:
At least an UL transmission scheme without grant is supported for URLLC
  Resource may or may not be shared among one or more users
    FFS: resource configuration details
  FFS other details of design

## Slide 3: Proposal
For UL URLLC transmission without grant, URLLC traffic data with/without preamble can be considered
  Traffic data and preamble may be sent in different times and/or in different frequencies
  Preamble structure may or may not reuse existing channel/signals
  Preamble and/or DMRS can be used for at least:
    UE activity detection
    Demodulation for the traffic data
    FFS: Resource indication of the traffic data
    FFS: UE identification
    Other uses not precluded