## Slide 1
3GPP TSG RAN WG1 Meeting #87 R1-1613746 Reno, USA, November 14-18, 2016
Agenda item: 7.1.3.3
WF on Type I & Type II CSI Feedback
Huawei, HiSilicon, China Unicom, Intel, Samsung, Ericsson, CATT, LGE, [Nokia, Alcatel-Lucent Shanghai Bell]

## Slide 2: Background
In RAN1#86bis, the following agreements were made:
NR supports CSI reporting with two types of spatial information feedback
  Type I feedback: Normal
    Codebook-based PMI feedback with normal spatial resolution
  Type II feedback: Enhanced
    “Explicit” feedback and/or codebook-based feedback with higher spatial resolution
  For Type I and II, CSI feedback per subband as well as wideband feedback are supported
  For Type I and II, beam-related feedback can be included

## Slide 3: Proposal
For Type I CSI, PMI codebook has at least two stages W = W1W2
  W1 codebook comprises of beam groups/vectors
    E.g. LTE W1 codebook
  FFS structure and configuration of W1 codebook, e.g. number of ports, grid of beams, orthogonal, non-orthogonal, beam broadening, etc
  FFS frequency granularity of W1 and W2 reporting
  FFS on additional support of W3 (location of W3 matrix is FFS), e.g. multi-panel support, analog beam selection
  Note multi-panel support may be captured in W1, W2 and/or W3
For Type II CSI,
  Study the following CSI feedback schemes
    Analog CSI feedback
    Linear combination based CSI feedback
      For example
        Projection of channel and/or covariance matrix and/or eigenvectors onto a basis
        Linear combination of a basis
        Schemes may have orthogonal and/or non-orthogonal basis
      Quantization examples
        Magnitude and phase
        Real and imaginary
        Vector quantization
    Precoder / Precoding Matrix
    Contents for Quantized or Unquantized CSI feedback
      Channel covariance matrix feedback
        e.g. Hermitian-form codebook, analog CSI feedback, linear combination codebook
      Channel Approximation and/or Measurement
        e.g. analog CSI feedback, linear combination codebook
      Channel Eigen vectors
        e.g. analog CSI feedback, linear combination codebook
      Other forms of channel representation are not excluded.