## Slide 1: WF on PDSCH resource allocation for 5 MHz in CE mode A in FeMTC
Ericsson, Lenovo
3GPP TSG-RAN WG1 Meeting #88 R1-1703595
Athens, Greece, 13th – 17th February 2017 Agenda Item: 7.2.3.1.1

## Slide 2: Proposal
For PDSCH resource allocation for 5 MHz in CE mode A, the number of bits in DCI for resource assignment is the same as in Rel-13.
Resource allocation for PDSCH within one 6-PRB narrowband in CE mode A is performed according to Rel-13, i.e.:
  MSBs are used to indicate the index of the allocated narrowband.
  5 LSBs are used for allocation within the narrowband using Rel-8 resource allocation type 2 where Resource Indication Value (RIV) is used to indicate the starting RB and length of allocation in terms of number of RB.
Resource allocation for PDSCH larger than one 6-PRB narrowband in CE mode A is indicated using some or all of the 11 currently unused values in the Rel-13 resource allocation field.
  The index of the first narrowband within the resource allocation is indicated using the MSBs in the resource assignment field in DCI.
  The resource allocation is within 4 consecutive narrowbands (corresponding to 24 PRBs) starting with the indicated narrowband.
  The mentioned 24 PRBs are divided into Resource Block Groups (RBGs) à 3 PRBs.

## Slide 3: Proposal on use of unused RA indices for PDSCH resource allocation in CE mode A
RA index | RBG #0 | RBG #1 | RBG #2 | RBG #3 | RBG #4 | RBG #5 | RBG #6 | RBG #7
10111 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0
11000 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0
11001 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
11010 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0
11011 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1
11100 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0
11101 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1
11110 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1
11111 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1