## Slide 1
3GPP TSG RAN WG1#88 Meeting
Athens, Greece ,13th - 17th Feb. 2017
Agenda item 8.1.4.1
R1-1703771
WF on LDPC Decoder Throughput Requirement
Samsung,

## Slide 2: Background
LDPC code decoder throughput is different according to effective code rate
  The decoder operates on the related parity-check matrix for effective rate, not the whole parity-check matrix
  Parity bits from single parity-check codes are of degree one, they, and their associated parity-check constraints, can be completely ignored by the decoder according to effective rate.

## Slide 3: Background
Transmission throughput requirement for eMBB scenario is 20Gbps
Decoder throughput requirement for LDPC codes is varied according to HARQ scenarios
Scenarios | Decoder Throughput
 | Support 20Gbps
Full IR-HARQ | with CR 1/3
Partial IR-HARQ | with CR 4/9
CC-HARQ | with CR 8/9
R1-1703002, Samsung, Consideration on Throughput and Latency for LDPC Code Design

## Slide 4: Proposal 1: Decoder throughput
Decoder throughput requirement should be decided
  Alt. 1 : Support 20Gbps with code rate 1/3 for full IR-HARQ
  Alt. 2 : Support 20Gbps with code rate 4/9 for partial IR-HARQ
  Alt. 3 : Support 20Gbps with code rate 8/9 for CC-HARQ

## Slide 5: Proposal 2:
The decoder configuration to support decoder throughput requirement should be provided.