## Slide 1: WF on CBR and CR definition for 36.214
Huawei, HiSilicon
3GPP TSG RAN WG1 Meeting #88 R1-1704035
Athens, Greece 13th - 17th February 2017
Agenda item – 7.2.1.3

## Slide 2: Proposal
Definition | Channel busy radio (CBR) measured at subframe n is defined as follows: For PSSCH, the portion of sub-channels in the resource pool whose S-RSSI measured by the UE exceed a (pre-)configured threshold sensed over subframes [n-99100, n-1], For PSCCH when in a pool (pre)configured such that PSCCH may be transmitted with its corresponding PSSCH in non-adjacent resource blocks, the portion of the sub-channels of the PSCCH pool whose S-RSSI measured by the UE exceed a (pre-)configured threshold sensed over subframes [n-99100, n-1], assuming that the PSCCH pool is composed of sub-channels with a size of two resource blocks.
NOTE: The subframe index is based on physical subframe index.

## Slide 3: Proposal
NOTE 1: a and b are positive integers determined by UE implementation with a+b+1 = 1000, a >= [500], and n+b should not exceed the last transmission opportunity of the grant for the current transmission.
NOTE 2: CR is evaluated for each (re)transmission.
NOTE 3: In evaluating CR, the UE shall assume the transmission parameter used at subframe n is reused according to the existing grant(s) in subframes [n+1, n+b] without packet dropping.
NOTE 4: The subframe index is based on physical subframe index.
Definition | Channel occupancy radio (CR) evaluated at subframe n is defined as the total number of sub-channels used for its transmissions in subframes [n-a, n-1] and granted in subframes [n, n+b] divided by the total number of configured sub-channels in the transmission pool over [n-a, n+b].