## Slide 1
3GPP TSG RAN WG1 Meeting #88bis R1-1706232
Spokane, USA, 3rd - 7th April 2017
Agenda item: 7.2.5.2
WF on DMRS density reduction
Huawei, HiSilicon, Qualcomm, China Telecom

## Slide 2: Background
In RAN#75, a new WID on Enhancements for high capacity stationary wireless link and introduction of 1024 QAM for LTE was approved. The following objective is agreed:
  Specify DM-RS overhead reduction using OCC4 for DL SU-MIMO rank3/4 in TM9/10 [RAN1]

## Slide 3: Proposals
Existing DMRS table is modified to support OCC4 DL rank 3/4 SU-MIMO transmission
  FFS: Define a new DMRS table or introduce new entries in existing DMRS table
  DCI payload size is the same as legacy
  Whether to support OCC4 DL rank 3/4 MU-MIMO transmission is FFS
Additional DMRS overhead reduction scheme for rank 3/4 transmission is FFS