## Slide 1: WF on frequency granularity for CSI reporting
LG Electronics, Samsung
R1-1706319
3GPP TSG RAN1 #88bis
Spokane, USA, April 3 – 7, 2017
Agenda Item: 8.1.2.3.1

## Slide 2: Background(1/2)[TR38.802]
CSI reporting band is defined as a collection of (contiguous or non-contiguous) subbands pertinent to a CSI reporting setting.

## Slide 3: Background(2/2)[TR38.802]
For CSI reporting for a component carrier, at least three different frequency granularities are supported.
  Wideband CSI
    Wideband size is determined by UE RF capability of receiving DL signal. Location of wideband could be configurable by network. For example, wideband CSI is used for analog beam management at least.
  Partial band CSI
    Alt1. UE-specifically configurable bandwidth
    Alt2. The size is determined by the composition of numerologies or scheduling time units within the UE-specific wideband.
      Applicable only when different numerology or scheduling time unit are multiplexed within wideband.
    For example, partial band CSI is used for analogue beam management and for managing CSI per service at least.
  Subband CSI
    The band size is determined by dividing wideband or partial band to multiple bands. For example, subband CSI is used for frequency selective scheduling and subband precoding at least.

## Slide 4: Proposals
For wideband CSI reporting, CSI reporting band is not configured.
For partial band CSI reporting, CSI reporting band is configured in the reporting setting.
For subband CSI reporting, CSI reporting band may or may not be configured in the reporting setting.
  If configured, subbands are confined within the configured band.
  If not configured, subbands are defined within the wideband.
  FFS: subband size is dependent on wideband size or partial band size.
For a given CSI reporting band, UE can assume that the same numerology and scheduling time unit is used.