## Slide 1: [draft] Way forward on supporting 64 QAM in PDSCH
Ericsson,[….]
R1-1706331
3GPP TSG RAN WG1 Meeting #88bis
Spokane, USA, April 3 - 7, 2017
Agenda item 7.2.6.5

## Slide 2: Background
The Rel-15 WI on “Even further enhanced MTC for LTE” (RP-170732) has the following WI objective for machine-type communications for BL/CE UEs:
  Increased PDSCH spectral efficiency [RAN1 lead, RAN2, RAN4]
    Specify optional support for 64QAM for unicast PDSCH (no UE peak rate increase is intended).

## Slide 3: Proposals
64QAM is supported only for Rel-15 efeMTC UEs configured with maximum PDSCH channel bandwidth of 1.4 or 5 MHz, and only for unicast PDSCH in CE mode A
  FFS whether 64 QAM can be used with repetitions.
Support for 64QAM by a Rel-15 efeMTC UE is indicated by capability signalling.
Use of 64QAM for a Rel-15 efeMTC UE is configured through RRC signaling and can be enabled or disabled by RRC signaling.

## Slide 4: Proposals
The size of the MCS filed in the DCI
  Alt1: Extend the size of MCS table compared to (f)eMTC, i.e., to increase the MCS field in DCI format 6-1A to 5 bits to support 64 QAM.
  Alt2: Replacing certain rows to include 64-QAM and keep the size of MCS table the same as in (f)eMTC.
The detailed MCS design is FFS