## Slide 1: WF on CSI-RS for beam management
Samsung, …
3GPP TSG-RAN WG1 Meeting #88b R1-170XXXX
Spokane, USA 3rd - 7th April 2017
Agenda item: 8.1.2.4.1
Document for decision

## Slide 2: Background
Agreement in RAN1 #87 meeting

## Slide 3: Background
Agreement in RAN1 #88 meeting

## Slide 4: Proposals
  Within a CSI-RS resource for beam management use case, CSI-RS ports can be mapped on the REs in the FDM manner in the CSI-RS BW
    CSI-RS resource can have configurability of sub-time units
    OFDM symbol(s) with CSI-RS can be configured to contain CSI-RS only within the CSI-RS BW
      FFS: CSI-RS with sub-time units can be FDMed with PDSCH within the CSI-RS BW
      FFS: CSI-RS with sub-time units can be FDMed with DMRS within the CSI-RS BW
      FFS: CSI-RS with sub-time units can be FDMed with SS blocks within the CSI-RS BW
    All the configured CSI-RS ports are cyclically mapped across the REs in the frequency domain
      Note: Some of REs can be defined as ZP-CSI-RS to support sub-time units using IFDMA
  A set of CSI-RS resources configured for beam management purpose can contain at least the following parameters:
    A number of sub-time units in a time unit

## Slide 5: Example of CSI-RS port mapping
NP = 8
…
…
…
…
…
…
…
…
NP = 4
NP = 2
NP = 1
Frequency domain