## Slide 1: WF on Scheduling Request Resources in Multi-beam Scenario
3GPP TSG RAN WG1 88bis R1-1706432
Spokane, USA
3rd – 7th April, 2017
Agenda item: 8.1.3.2.3
Document for decision

## Slide 2: Background - I
If UL data arrives, UEs need to transmit scheduling request to get resources for sending UL buffer status report
In multi-beam scenario, if a UE has not been allocated PUCCH resources, it needs to transmit SR in a region where gNB will listen to it
SR resources need to be allocated in a region where gNB listens from all directions
Transmitting RACH is an option. But it is inefficient because the number of preambles is limited by round trip delay
  Much higher number of preambles can be accommodated if UEs are time synchronized

## Slide 3: Background - II
NR has agreed on following procedure for beam recovery [1]
The following mechanisms should be supported in NR:
  The UL transmission to report beam failure can be located in the same time instance as PRACH:
    Resources orthogonal to PRACH resources
      FFS orthogonal in frequency and/or sequences (not intended to impact PRACH design)
      FFS channels/signals
  The UL transmission to report beam failure can be located at a time instance (configurable for a UE) different from PRACH
    Consider the impact of RACH periodicity in configuring the UL signal to report beam failure located in slots outside PRACH
    FFS the signal/channel for the UL transmission
  Additional mechanisms using other channels/signals are not precluded (e.g., SR, UL grant free PUSCH, UL control)
Scheduling request to get resources for sending UL buffer can be transmitted in the same way but it does not need to go through the full beam recovery procedure
1. R1-1703571, UL signal design for beam recovery request, 3GPP TSG RAN WG1 88

## Slide 4: Example: SR Region in RACH Slot
 | …. |  |  |  |  |  |  |  | 
SR region
RACH region
gNB sweeps synchronization signals in different beam directions.
UE measures the quality of reference signal and selects a suitable beam
If UE is time synchronized, it transmits scheduling request in the SR region [2, 3]
  Higher number of UEs can be accommodated in this region
If UE is not time synchronized, it goes through the RACH procedure
2. R1-1706171, “PRACH design consideration”, Qualcomm Inc, 3GPP TSG RAN WG1 88bis
3. R1-1702606, “Beam Recovery Procedure”, Qualcomm Inc., 3GPP TSG RAN WG1 88

## Slide 5: Proposal
NR supports scheduling request region in multi-beam scenario
Network explicitly configures the UEs with resources for transmitting scheduling request in a region where the base station is listening from all or partial directions
  e.g. random access slot
UE can choose only a subset of resources based on the quality of some DL reference signals such as SSS
NR studies if UEs can transmit SR with the same baseline sequence as RACH sequence
  NR studies if higher number of cyclic shifts can be accommodated to transmit SR