## Slide 1: WF on evaluation assumptions for aerials study
Ericsson, NTT DOCOMO, Intel
R1-1706475
3GPP TSG RAN WG1 Meeting #88bis
Spokane, USA, 3rd – 7th April 2017
Agenda item 7.2.8.2

## Slide 2: Background
The objective of the study item is to study the ability for aerial vehicles to be served using LTE network deployments with base station antennas targeting terrestrial coverage, supporting Release 14 functionality (i.e. including active antennas and FD-MIMO)
Rural and urban scenarios are two important scenarios for performance evaluation in this study item

## Slide 3: Proposal
The following evaluation assumptions are used for the aerial study
Parameters |  | UMi AV (optional) | UMa AV | RMa AV
Cell layout |  | Hexagonal grid, 19 micro sites, 3 sectors per site (ISD = 200m) FFS: if 37 micro sites, 3 sectors per site are needed | Hexagonal grid, 19 macro sites, 3 sectors per site (ISD = 500m) FFS: if 37 macro sites, 3 sectors per site are needed | Hexagonal grid, 19 macro sites, 3 sectors per site (ISD = 1732m; FFS: ISD = 3000m) FFS: if 37 macro sites, 3 sectors per site are needed
BS antenna height |  | 10m | 25m | 35m
Carrier frequency |  | 2GHz | 2 GHz | 700 MHz; FFS: 800 MHz
Total BS Tx power |  | 41/44 dBm for 10/20MHz | 46/49 dBm for 10/20MHz | 46/49 dBm for 10/20MHz
BS antenna configuration |  | Baseline: 2Tx/2Rx cross polarized For FD-MIMO: FFS | Baseline: 2Tx/2Rx cross polarized For FD-MIMO: FFS | Baseline: 2Tx/2Rx cross polarized For FD-MIMO: FFS
BS antenna pattern |  | FFS | FFS | FSS
BS antenna element pattern |  | For FD-MIMO, according to TR38.901 | For FD-MIMO, according to TR38.901 | For FD-MIMO, according to TR38.901
BS antenna element gain + connector loss |  | 8dBi | 8dBi | 8dBi
UT location | Outdoor terrestrial/indoor terrestrial/aerial | Outdoor terrestrial and indoor terrestrial (same as UMi/UMa in TR38.901), and aerial (new UT type) |  | Outdoor terrestrial and indoor terrestrial (same as RMa in TR38.901), and aerial (new UT type)
 | LOS/NLOS (terrestrial) | LOS and NLOS |  | 
 | LOS/NLOS (aerial) | FFS | FFS | FFS
 | Height (terrestrial) | Baseline: 1.5m for indoor terrestrial and outdoor terrestrial UTs For FD-MIMO: Same as UMi in TR 38.901 | Baseline: 1.5m for indoor terrestrial and outdoor terrestrial UTs For FD-MIMO: Same as UMa in TR38.901 | Same as RMa in TR38.901
 | Height (aerial) | Uniformly distributed between FFS and FFS Optionally: FFS fixed height values | Uniformly distributed between FFS and FFS Optionally: FFS fixed height values | Uniformly distributed between FFS and FFS Optionally: FFS fixed height values
Parameters |  | UMi AV (optional) | UMa AV | RMa AV
Cell layout |  | Hexagonal grid, 19 micro sites, 3 sectors per site (ISD = 200m) FFS: if 37 micro sites, 3 sectors per site are needed | Hexagonal grid, 19 macro sites, 3 sectors per site (ISD = 500m) FFS: if 37 macro sites, 3 sectors per site are needed | Hexagonal grid, 19 macro sites, 3 sectors per site (ISD = 1732m; FFS: ISD = 3000m) FFS: if 37 macro sites, 3 sectors per site are needed
BS antenna height |  | 10m | 25m | 35m
Carrier frequency |  | 2GHz | 2 GHz | 700 MHz; FFS: 800 MHz
Total BS Tx power |  | 41/44 dBm for 10/20MHz | 46/49 dBm for 10/20MHz | 46/49 dBm for 10/20MHz
BS antenna configuration |  | Baseline: 2Tx/2Rx cross polarized For FD-MIMO: FFS | Baseline: 2Tx/2Rx cross polarized For FD-MIMO: FFS | Baseline: 2Tx/2Rx cross polarized For FD-MIMO: FFS
BS antenna pattern |  | FFS | FFS | FSS
BS antenna element pattern |  | For FD-MIMO, according to TR38.901 | For FD-MIMO, according to TR38.901 | For FD-MIMO, according to TR38.901
BS antenna element gain + connector loss |  | 8dBi | 8dBi | 8dBi
UT location | Outdoor terrestrial/indoor terrestrial/aerial | Outdoor terrestrial and indoor terrestrial (same as UMi/UMa in TR38.901), and aerial (new UT type) |  | Outdoor terrestrial and indoor terrestrial (same as RMa in TR38.901), and aerial (new UT type)
 | LOS/NLOS (terrestrial) | LOS and NLOS |  | 
 | LOS/NLOS (aerial) | FFS | FFS | FFS
 |  | Baseline: 1.5m for indoor terrestrial and outdoor terrestrial UTs For FD-MIMO: Same as UMi in TR 38.901 | Baseline: 1.5m for indoor terrestrial and outdoor terrestrial UTs For FD-MIMO: Same as UMa in TR38.901 | Same as RMa in TR38.901
 |  | Uniformly distributed between FFS and FFS Optionally: FFS fixed height values | Uniformly distributed between FFS and FFS Optionally: FFS fixed height values | Uniformly distributed between FFS and FFS Optionally: FFS fixed height values

## Slide 4: Proposal (cont’d)
Parameters | UMi AV (optional) | UMa AV | RMa AV
Indoor terrestrial UT ratio defined as | 80% | 80% | 50%
Outdoor terrestrial UT ratio defined as | 20% | 20% | 50%
Aerial UT ratio defined as | FFS | FFS | FFS
Number of indoor terrestrial UTs + outdoor terrestrial UTs + aerial UTs | [10] per cell Note: the number of total terrestrial UTs can be varied to achieve different aerial UT ratios | [10] per cell Note: the number of total terrestrial UTs can be varied to achieve different aerial UT ratios | [10] per cell Note: the number of total terrestrial UTs can be varied to achieve different aerial UT ratios
UT mobility (horizontal plane only) | FFS | FFS | FFS
Min. BS – UT distance (2D) | 10m | 35m | 35m
UT distribution (horizontal) – for outdoor terrestrial/indoor terrestrial/aerial | Uniform | Uniform | Uniform
Channel models for terrestrial UT | According to TR 38.901 | According to TR 38.901 | According to TR 38.901
Channel models for aerial UT | FFS | FFS | FFS
Parameters | UMi AV (optional) | UMa AV | RMa AV
 | 80% | 80% | 50%
 | 20% | 20% | 50%
 | FFS | FFS | FFS
Number of indoor terrestrial UTs + outdoor terrestrial UTs + aerial UTs | [10] per cell Note: the number of total terrestrial UTs can be varied to achieve different aerial UT ratios | [10] per cell Note: the number of total terrestrial UTs can be varied to achieve different aerial UT ratios | [10] per cell Note: the number of total terrestrial UTs can be varied to achieve different aerial UT ratios
UT mobility (horizontal plane only) | FFS | FFS | FFS
Min. BS – UT distance (2D) | 10m | 35m | 35m
UT distribution (horizontal) – for outdoor terrestrial/indoor terrestrial/aerial | Uniform | Uniform | Uniform
Channel models for terrestrial UT | According to TR 38.901 | According to TR 38.901 | According to TR 38.901
Channel models for aerial UT | FFS | FFS | FFS

## Slide 5: Proposal (cont’d)
Parameters | UMi AV (optional) | UMa AV | RMa AV
Terrestrial UT Tx Power | 23dBm | 23dBm | 23dBm
Aerial UT Tx Power | 23dBm | 23dBm | 23dBm
Tterrestrial or aerial UT antenna element pattern | Omni-directional | Omni-directional | Omni-directional
Terrestrial or aerial UT antenna element gain | 0dBi | 0dBi | 0dBi
Number of terrestrial or aerial UT antennas | FFS | FFS | FFS
BS receiver noise figure | 5dB | 5dB | 5dB
Terrestrial/aerial UT receiver noise figure | 9dB | 9dB | 9dB
Baseline receiver for terrestrial/aerial UT | MMSE-IRC |  | 
Feedback assumption | Non-ideal |  | 
Channel estimation | Non-ideal |  |