## Slide 1: WF on Traffic Requirements for Aerial Vehicles
Nokia, Alcatel-Lucent Shanghai Bell, ZTE, ZTE Microelectronics, Tongji University
R1-1706476
3GPP TSG RAN WG1 Meeting #88bis
Spokane, USA, April 3rd – 7th 2017
Agenda item 7.2.8.1

## Slide 2: Background
A new Study Item on “Study on Enhanced Support for Aerial Vehicles” was approved at RAN#75 meeting with the target of enhanced support for aerial vehicles served by LTE network.
The aerial vehicles are connected to a UAV pilot on the ground today, while in the future the control may be given to a traffic control system. The control link has a relatively low data rate, but requires higher reliability and relatively low latency.
The aerial vehicles may support one or more application(s) with higher data rate requirement, for example flying cameras, to support live stream in the uplink.

## Slide 3: Proposals
  Proposal 1: The traffic requirements for aerial vehicles are
  Control traffic
    Data rate: 30 kbps in uplink and downlink
    Air interface one way delay: 50 ms
    Reliability: [99.9%]
  Application-based traffic
    Data rate: 10 Mbps in uplink and [100] kbps in downlink
    Air interface one way delay: Best effort
    Reliability: [95%]

## Slide 4: Proposals
  Proposal 2: Capture the traffic requirements in Table 1 into TR.
 | UAV control traffic | Application based traffic
Data rate | 30 kbps in uplink and downlink | 10 Mbps in uplink [100] kbps in downlink
Air interface one way delay | 50 ms | Best effort
Reliability | [99.9] % | [95] %
Table 1 Traffic requirements for drones