## Slide 1: Way forward on simulation assumptions for reduced system acquisition time
Ericsson, Sierra Wireless, ..
R1-1706501
3GPP TSG RAN WG1 Meeting #88bis
Spokane, USA, April 3 - 7, 2017
Agenda item 7.2.6.1

## Slide 2: Background
During RAN1#88bis, agreements on reduced system acquisition time are achieved as follows:
  Techniques for system acquisition time reduction to be considered:
  PSS/SSS
    Enhanced (e.g. repeated) PSS/SSS based on PSS/SSS or NPSS/NSSS design
    Use of NPSS/NSSS on NB-IoT anchor carrier
  PBCH
    Enhanced (e.g. repeated) PBCH based on PBCH or NPBCH design
    Use of NPBCH on NB-IoT anchor carrier
    Combining across 40-ms PBCH periods (unless already part of Rel-14 demodulation requirements)
    New mechanism allowing to skip MIB message reading
  SIB1-BR
    Additional repetitions of SIB1-BR
    Accumulation across SIB1-BR modification periods (unless already part of Rel-14 demodulation requirements)
    New mechanism allowing to skip SIB1-BR reading
      E.g. SI update indication or other indication in MIB or another channel
  SI messages
    Additional repetitions of SI messages
    New mechanism allowing to skip SI message reading
      E.g. SI update indication or other indication in MIB or another channel

## Slide 3: Proposal
  To evaluate the techniques for system acquisition time reduction the following assumptions are proposed:
    Metrics for evaluating performance of acquisition of downlink frame synchronization, MIB, SIB1-BR and SI messages:
    Assumptions for evaluating performance of acquisition of downlink frame synchronization, MIB, SIB1-BR and SI messages:
Performance Metric | Unit
Acquisition time @ 50th, 90th percentile | ms
False detection rate | % (expressed as part of false detection events)
Device complexity | % (expressed as increase compared to Rel-13 Cat M1)
System overhead | % (expressed as used part of REs per radio frame)
Parameter | Value
BS TX antenna configuration | 2 Tx
BS power | 43 dBm per TX port
System BW | 10 MHz
Band | Band 8 (900 MHz)
Channel model | ETU
Doppler spread | 1 Hz
Initial frequency error @ acquisition of PSS | ±5 ppm
Frequency error @ acquisition of SSS, PBCH, PDSCH | ±30 Hz
UE RX antenna configuration | 1 Rx
UE NF | 5, 9 dB
Coupling loss | 144, 154, 164 dB