## Slide 1: WF on Beam-Related Indication
Ericsson, Intel, ZTE, …
3GPP TSG RAN WG1 Meeting #88bis
Spokane, USA, 3rd – 7th April 2017
Agenda item 8.1.2.2.1
R1-17xxxxx

## Slide 2: Previous Agreements
Agreement:
For downlink, NR supports beam management with and without beam-related indication
  When beam-related indication is provided, information pertaining to UE-side beamforming/receiving procedure used for data reception can be indicated through QCL to UE
    FFS: Information other than QCL
  FFS: When beam-related indication is provided, information pertaining to the Tx beam used for data transmission is indicated to UE
Agreement:
Indication of QCL between the antenna ports of two CSI-RS resources is supported.
  By default, no QCL should be assumed between antenna ports of two CSI-RS resources.
  Partial QCL parameters (e.g., only spatial QCL parameter at UE side) should be considered.
For downlink, NR supports CSI-RS reception with and without beam-related indication,
  When beam-related indication is provided, information pertaining to UE-side beamforming/receiving procedure used for CSI-RS-based measurement can be indicated through QCL to UE
  QCL information includes spatial parameter(s) for UE side reception of CSI-RS ports
    FFS: information other than QCL

## Slide 3: Previous Agreements
Agreement:
For reception of unicast DL data channel, support indication of spatial QCL assumption between DL RS antenna port(s) and DMRS antenna port(s) of DL data channel: Information indicating the RS antenna port(s) is indicated via DCI (downlink grants)
  The information indicates the RS antenna port(s) which is QCL-ed with DMRS antenna port(s)
    FFS: Indication details
      E.g. explicit indication of RS port/resource ID, or implicitly derived
  FFS when the indication is applied (e.g., the indication is assumed only for the scheduled PDSCH or until next indication; when the above information is included, if there should be a scheduling/beam switch offset, etc.)
  FFS: Beam indication for receiving fall back unicast PDSCH (if supported)
  Note: related signalling is UE-specific

## Slide 4: Proposal
For DL beam management, when multiple links between the gNB and UE are maintained for the purposes of data and/or control channel transmission/reception, NR supports the following
  Indication of spatial QCL assumption to assist UE-side beamforming/receiving in the form of a N-bit tag where the tag implicitly refers to one or more CSI-RS resource(s)/port(s) transmitted in one or more previous slots
  For reception of CSI-RS, the tag indicates spatial QCL between one or more current CSI-RS resource(s)/port(s) and one or more CSI-RS resource(s)/port(s) transmitted in one or more previous slot(s)
  For reception of PDSCH/PDCCH, the tag indicates spatial QCL between DMRS for PDSCH/PDCCH and one or more CSI-RS resource(s)/port(s) in one or more previous slot(s)
To support multi-beam transmissions, FFS whether one tag or multiple tags are needed for reference to multiple CSI-RS resource(s)/port(s) in one or more previous slot(s)
FFS: value of N where N is chosen to ensure low overhead, e.g., N = 2
FFS: tag for indicating QCL to other reference signals, e.g., SS, RS for mobility
FFS: indication method, e.g., DCI, MAC-CE, RRC